ПРИЛОЖЕНИЕ А3

ТЕХНИЧЕСКО ОПИСАНИЕ

Обособена позиция № 3. Мрежово оборудване

1. Мрежов комутатор 1

| Наименование: | Мрежов комутатор 1 |
| --- | --- |
| Марка: | /попълва се от участника/ |
| Модел: | /попълва се от участника/ |
| URL от сайт на производителя: | /попълва се от участника/ |
| Гаранционен срок | >= | 24 месеца | /предложение/ |
| ОСНОВНИ ХАРАКТЕРИСТИКИ | Съвместимост с PacketFence NAC версия 8.1 https://packetfence.org/about.html#/material | = | ДА | /предложение/ |
|  | Rackmount, 1U hight | = | ДА | /предложение/ |
|  | Total Non-Blocking Throughput | >= | 16 Gbps | /предложение/ |
|  | Switching Capacity | >= | 32 Gbps | /предложение/ |
|  | Forwarding Rate | >= | 23,81 Mpps | /предложение/ |
|  | Max. AC Power Consumption | <= | 56 W | /предложение/ |
|  | Power Specs | DC Input Option (Redundant or Stand-Alone) | = | ДА | /предложение/ |
|  |  | AC | 100-240VAC/50-60 Hz, Universal Input | = | ДА | /предложение/ |
|  |  | DC | DC 56W, 25 to 16V, with 2.5 mm DC Power Inline Connector | = | ДА | /предложение/ |
|  |  | Supported Voltage Range | 100 to 240VAC | = | ДА | /предложение/ |
|  |  |  | 25 to 16VDC | = | ДА | /предложение/ |
|  | Interfaces | Networking Interfaces | Total number of ports | >= | 16 | /предложение/ |
|  |  |  | 100/1000 Mbps SFP Ethernet Ports | >= | 8 | /предложение/ |
|  |  |  | 1000 Mbps SFP Ethernet Ports | >= | 4 | /предложение/ |
|  |  |  | 10/100/1000 Mbps RJ45 Ethernet Ports | >= | 4 | /предложение/ |
|  |  | Management Interface | RJ45 Serial Port | >= | 1 | /предложение/ |
|  |  |  | Ethernet In/Out Band | = | ДА | /предложение/ |
|  | Operating Temperature | -5 to 40° C | = | ДА | /предложение/ |
|  | Operating Humidity | 5 to 95% Noncondensing | = | ДА | /предложение/ |
| CORE SWITCHING FEATURES | ANSI/TIA-1057: LLDP-Media Endpoint Discovery (MED) | = | ДА | /предложение/ |
|  | EEE 802.1AB: Link Layer Discovery Protocol (LLDP) | = | ДА | /предложение/ |
|  | EEE 802.1D: Spanning Tree Compatibility | = | ДА | /предложение/ |
|  | IEEE 802.1S: Multiple Spanning Tree Compatibility | = | ДА | /предложение/ |
|  | IEEE 802.1W: Rapid Spanning Tree Compatibility | = | ДА | /предложение/ |
|  | IEEE 802.1Q: Virtual LANs with Port-Based VLANs | = | ДА | /предложение/ |
|  | IEEE 802.1p: Ethernet Priority with User Provisioning and Mapping | = | ДА | /предложение/ |
|  | EEE 802.1X: Port-Based Authentication with Guest VLAN Support | = | ДА | /предложение/ |
|  | EEE 802.3: 10BASE-T | = | ДА | /предложение/ |
|  | IEEE 802.3u: 100BASE-T | = | ДА | /предложение/ |
|  | EEE 802.3ab: 1000BASE-T | = | ДА | /предложение/ |
|  | IEEE 802.1ak: Virtual Bridged Local Area Networks - Amendment 07: Multiple Registration Protocol | = | ДА | /предложение/ |
|  | IEEE 802.3ac: VLAN Tagging | = | ДА | /предложение/ |
|  | IEEE 802.3ad: Link Aggregation | = | ДА | /предложение/ |
|  | IEEE 802.3x: Flow Control | = | ДА | /предложение/ |
|  | IEEE 802.1D-2004: Generic Attribute Registration Protocol: Clause 12 (GARP) | = | ДА | /предложение/ |
|  | IEEE 802.1D-2004: Dynamic L2 multicast registration: Clause 10 (GMRP) | = | ДА | /предложение/ |
|  | IEEE 802.1Q-2003: Dynamic VLAN registration: Clause 11.2 (GVRP) | = | ДА | /предложение/ |
|  | RFC 4541: Considerations for Internet Group Management Protocol (IGMP) Snooping Switches | = | ДА | /предложение/ |
|  | RFC 5171: Unidirectional Link Detection (UDLD) Protocol | = | ДА | /предложение/ |
| ADVANCED LAYER 2 FEATURES | Broadcast Storm Recovery | = | ДА | /предложение/ |
|  | Broadcast/Multicast/Unknown Unicast Storm Recovery | = | ДА | /предложение/ |
|  | DHCP Snooping | = | ДА | /предложение/ |
|  | IGMP Snooping Querier | = | ДА | /предложение/ |
|  | Independent VLAN Learning (IVL) Support | = | ДА | /предложение/ |
|  | Jumbo Ethernet Frame Support | = | ДА | /предложение/ |
|  | Port MAC Locking | = | ДА | /предложение/ |
|  | Port Mirroring | = | ДА | /предложение/ |
|  | Protected Ports | = | ДА | /предложение/ |
|  | Static MAC Filtering | = | ДА | /предложение/ |
|  | TACACS+ | = | ДА | /предложение/ |
|  | Voice VLANs | = | ДА | /предложение/ |
|  | Unauthenticated VLAN | = | ДА | /предложение/ |
|  | Internal 802.1X Authentication Server | = | ДА | /предложение/ |
| PLATFORM SPECIFICATIONS | DHCP Server | Maximum Number of Pools: | >= | 8 | /предложение/ |
|  |  | Maximum Number of Leases (Total): | >= | 128 | /предложение/ |
|  | Routing | Number of Routes: | >= | 16 | /предложение/ |
|  |  | Number of Routing Interfaces: | >= | 15 | /предложение/ |
|  | VLANs: | >= | 255 | /предложение/ |
|  | MAC Addresses: | >= | 8000 | /предложение/ |
|  | MSTP Instances: | >= | 4 | /предложение/ |
|  | LAGs | >= | 6 | /предложение/ |
|  | Traffic Classes (Queues) | >= | 8 | /предложение/ |
| SYSTEM FACILITIES | Event and Error Logging Facility | = | ДА | /предложение/ |
|  | Run-Time and Configuration Download Capability | = | ДА | /предложение/ |
|  | PING Utility | = | ДА | /предложение/ |
|  | FTP/TFTP Transfers via IPv4/IPv6 | = | ДА | /предложение/ |
|  | Malicious Code Detection | = | ДА | /предложение/ |
|  | BootP and DHC | = | ДА | /предложение/ |
|  | RFC 2021: Remote Network Monitoring Management Information Base Version 2 | = | ДА | /предложение/ |
|  | RFC 2030: Simple Network Time Protocol (SNTP | = | ДА | /предложение/ |
|  | RFC 2819: Remote Network Monitoring Management Information Base | = | ДА | /предложение/ |
|  | RFC 2865: RADIUS Client | = | ДА | /предложение/ |
|  | RFC 2866: RADIUS Accounting | = | ДА | /предложение/ |
|  | RFC 2868: RADIUS Attributes for Tunnel Protocol Support | = | ДА | /предложение/ |
|  | RFC 2869: RADIUS Extensions | = | ДА | /предложение/ |
|  | RFC 3579: RADIUS Support for EAP | = | ДА | /предложение/ |
|  | RFC 3580: IEEE 802.1X RADIUS Usage Guidelines | = | ДА | /предложение/ |
|  | RFC 3164: BSD Syslog Protocol | = | ДА | /предложение/ |
| MANAGEMENT | Web UI | = | ДА | /предложение/ |
|  | Industry-Standard CLI | = | ДА | /предложение/ |
|  | IPv6 Management | = | ДА | /предложение/ |
|  | Password Management | = | ДА | /предложение/ |
|  | Autoinstall Support for Firmware Images and Configuration Files | = | ДА | /предложение/ |
|  | SNMP v1, v2, and v3 | = | ДА | /предложение/ |
|  | SSH 1.5 and 2.0 | = | ДА | /предложение/ |
|  | SSL 3.0 and TLS 1.0 | = | ДА | /предложение/ |
|  | Secure Copy (SCP) | = | ДА | /предложение/ |
|  | Telnet (Multi-Session Support) | = | ДА | /предложение/ |
| QoS | Access Control Lists (ACLs) Permit/Deny Actions for Inbound IP and Layer 2 Traffic Classification Based on: | Time-Based ACL | = | ДА | /предложение/ |
|  |  | Source/Destination IP Address | = | ДА | /предложение/ |
|  |  | TCP/UDP Source/Destination Port | = | ДА | /предложение/ |
|  |  | IP Protocol Type | = | ДА | /предложение/ |
|  |  | Type of Service (ToS) or Differentiated Services (DSCP) Field | = | ДА | /предложение/ |
|  |  | Source/Destination MAC Address | = | ДА | /предложение/ |
|  |  | EtherType | = | ДА | /предложение/ |
|  |  | IEEE 802.1p User Priority | = | ДА | /предложение/ |
|  |  | VLAN ID | = | ДА | /предложение/ |
|  |  | RFC 1858: Security Considerations for IP Fragment Filtering | = | ДА | /предложение/ |
|  | Optional ACL Rule Attributes | Assign Flow to a Specific Class of Service (CoS) Queue | = | ДА | /предложение/ |
|  |  | Redirect Matching Traffic Flows | = | ДА | /предложение/ |
|  | Differentiated Services (DiffServ) | Classify Traffic Based on Same Criteria as ACLs | = | ДА | /предложение/ |
|  |  | Mark the IP DSCP or Precedence Header Fields, Optional | = | ДА | /предложение/ |
|  |  | Police the Flow to a Specific Rate with Two-Color Aware Support | = | ДА | /предложение/ |
|  |  | RFC 2474: Definition of the Differentiated Services Field (DS field) in the IPv4 and IPv6 Headers | = | ДА | /предложение/ |
|  |  | RFC 2475: An Architecture for Differentiated Services | = | ДА | /предложение/ |
|  |  | RFC 2597: Assured Forwarding Per-Hop Behavior (PHB) Group | = | ДА | /предложение/ |
|  |  | RFC 3246: An Expedited Forwarding PHB | = | ДА | /предложение/ |
|  |  | RFC 3260: New Terminology and Clarifications for DiffServ | = | ДА | /предложение/ |
|  | Class of Service (CoS) Queue Mapping Configuration | AutoVoIP: Automatic CoS Settings for VoIP | = | ДА | /предложение/ |
|  |  | IP DSCP-to-Queue Mapping | = | ДА | /предложение/ |
|  |  | Configurable Interface Trust Mode (IEEE 802.1p, DSCP, or Untrusted) | = | ДА | /предложение/ |
|  |  | Interface Egress Shaping Rate | = | ДА | /предложение/ |
|  |  | Strict Priority versus Weighted Scheduling per Queue | = | ДА | /предложение/ |

2. Мрежов комутатор 2

| Наименование: | Мрежов комутатор 2 |
| --- | --- |
| Марка: | /попълва се от участника/ |
| Модел: | /попълва се от участника/ |
| URL от сайт на производителя: | /попълва се от участника/ |
| Гаранционен срок | >= | 24 месеца | /предложение/ |
| ОСНОВНИ ХАРАКТЕРИСТИКИ | Съвместимост с PacketFence NAC версия 8.1 https://packetfence.org/about.html#/material | = | ДА | /предложение/ |
|  | Rackmount, 1U hight | = | ДА | /предложение/ |
|  | Total Non-Blocking Throughput | >= | 26 Gbps | /предложение/ |
|  | Switching Capacity | >= | 52 Gbps | /предложение/ |
|  | Forwarding Rate | >= | 38,69 Mpps | /предложение/ |
|  | Max. AC Power Consumption | <= | 25 W | /предложение/ |
|  | Power Specs | DC Input Option (Redundant or Stand-Alone) | = | ДА | /предложение/ |
|  |  | AC | 100-240VAC/50-60 Hz, Universal Input | = | ДА | /предложение/ |
|  |  | DC | DC 56W, 25 to 16V, with 2.5 mm DC Power Inline Connector | = | ДА | /предложение/ |
|  |  | Supported Voltage Range | 100 to 240VAC | = | ДА | /предложение/ |
|  |  |  | 25 to 16VDC | = | ДА | /предложение/ |
|  | Interfaces | Networking Interfaces | Total number of ports | >= | 26 | /предложение/ |
|  |  |  | 1 Gbps SFP Ethernet Ports | >= | 2 | /предложение/ |
|  |  |  | 10/100/1000 Mbps RJ45 Ethernet Ports | >= | 24 | /предложение/ |
|  |  | Management Interface | RJ45 Serial Port | >= | 1 | /предложение/ |
|  |  |  | Ethernet In/Out Band | = | ДА | /предложение/ |
|  | Operating Temperature | -5 to 40° C | = | ДА | /предложение/ |
|  | Operating Humidity | 5 to 95% Noncondensing | = | ДА | /предложение/ |
| CORE SWITCHING FEATURES | ANSI/TIA-1057: LLDP-Media Endpoint Discovery (MED) | = | ДА | /предложение/ |
|  | EEE 802.1AB: Link Layer Discovery Protocol (LLDP) | = | ДА | /предложение/ |
|  | EEE 802.1D: Spanning Tree Compatibility | = | ДА | /предложение/ |
|  | IEEE 802.1S: Multiple Spanning Tree Compatibility | = | ДА | /предложение/ |
|  | IEEE 802.1W: Rapid Spanning Tree Compatibility | = | ДА | /предложение/ |
|  | IEEE 802.1Q: Virtual LANs with Port-Based VLANs | = | ДА | /предложение/ |
|  | IEEE 802.1p: Ethernet Priority with User Provisioning and Mapping | = | ДА | /предложение/ |
|  | EEE 802.1X: Port-Based Authentication with Guest VLAN Support | = | ДА | /предложение/ |
|  | EEE 802.3: 10BASE-T | = | ДА | /предложение/ |
|  | IEEE 802.3u: 100BASE-T | = | ДА | /предложение/ |
|  | EEE 802.3ab: 1000BASE-T | = | ДА | /предложение/ |
|  | IEEE 802.1ak: Virtual Bridged Local Area Networks - Amendment 07: Multiple Registration Protocol | = | ДА | /предложение/ |
|  | IEEE 802.3ac: VLAN Tagging | = | ДА | /предложение/ |
|  | IEEE 802.3ad: Link Aggregation | = | ДА | /предложение/ |
|  | IEEE 802.3x: Flow Control | = | ДА | /предложение/ |
|  | IEEE 802.1D-2004: Generic Attribute Registration Protocol: Clause 12 (GARP) | = | ДА | /предложение/ |
|  | IEEE 802.1D-2004: Dynamic L2 multicast registration: Clause 10 (GMRP) | = | ДА | /предложение/ |
|  | IEEE 802.1Q-2003: Dynamic VLAN registration: Clause 11.2 (GVRP) | = | ДА | /предложение/ |
|  | RFC 4541: Considerations for Internet Group Management Protocol (IGMP) Snooping Switches | = | ДА | /предложение/ |
|  | RFC 5171: Unidirectional Link Detection (UDLD) Protocol | = | ДА | /предложение/ |
| ADVANCED LAYER 2 FEATURES | Broadcast Storm Recovery | = | ДА | /предложение/ |
|  | Broadcast/Multicast/Unknown Unicast Storm Recovery | = | ДА | /предложение/ |
|  | DHCP Snooping | = | ДА | /предложение/ |
|  | IGMP Snooping Querier | = | ДА | /предложение/ |
|  | Independent VLAN Learning (IVL) Support | = | ДА | /предложение/ |
|  | Jumbo Ethernet Frame Support | = | ДА | /предложение/ |
|  | Port MAC Locking | = | ДА | /предложение/ |
|  | Port Mirroring | = | ДА | /предложение/ |
|  | Protected Ports | = | ДА | /предложение/ |
|  | Static MAC Filtering | = | ДА | /предложение/ |
|  | TACACS+ | = | ДА | /предложение/ |
|  | Voice VLANs | = | ДА | /предложение/ |
|  | Unauthenticated VLAN | = | ДА | /предложение/ |
|  | Internal 802.1X Authentication Server | = | ДА | /предложение/ |
| PLATFORM SPECIFICATIONS | DHCP Server | Maximum Number of Pools: | >= | 8 | /предложение/ |
|  |  | Maximum Number of Leases (Total): | >= | 128 | /предложение/ |
|  | Routing | Number of Routes: | >= | 16 | /предложение/ |
|  |  | Number of Routing Interfaces: | >= | 15 | /предложение/ |
|  | VLANs: | >= | 255 | /предложение/ |
|  | MAC Addresses: | >= | 8000 | /предложение/ |
|  | MSTP Instances: | >= | 4 | /предложение/ |
|  | LAGs | >= | 6 | /предложение/ |
|  | Traffic Classes (Queues) | >= | 8 | /предложение/ |
| SYSTEM FACILITIES | Event and Error Logging Facility | = | ДА | /предложение/ |
|  | Run-Time and Configuration Download Capability | = | ДА | /предложение/ |
|  | PING Utility | = | ДА | /предложение/ |
|  | FTP/TFTP Transfers via IPv4/IPv6 | = | ДА | /предложение/ |
|  | Malicious Code Detection | = | ДА | /предложение/ |
|  | BootP and DHC | = | ДА | /предложение/ |
|  | RFC 2021: Remote Network Monitoring Management Information Base Version 2 | = | ДА | /предложение/ |
|  | RFC 2030: Simple Network Time Protocol (SNTP | = | ДА | /предложение/ |
|  | RFC 2819: Remote Network Monitoring Management Information Base | = | ДА | /предложение/ |
|  | RFC 2865: RADIUS Client | = | ДА | /предложение/ |
|  | RFC 2866: RADIUS Accounting | = | ДА | /предложение/ |
|  | RFC 2868: RADIUS Attributes for Tunnel Protocol Support | = | ДА | /предложение/ |
|  | RFC 2869: RADIUS Extensions | = | ДА | /предложение/ |
|  | RFC 3579: RADIUS Support for EAP | = | ДА | /предложение/ |
|  | RFC 3580: IEEE 802.1X RADIUS Usage Guidelines | = | ДА | /предложение/ |
|  | RFC 3164: BSD Syslog Protocol | = | ДА | /предложение/ |
| MANAGEMENT | Web UI | = | ДА | /предложение/ |
|  | Industry-Standard CLI | = | ДА | /предложение/ |
|  | IPv6 Management | = | ДА | /предложение/ |
|  | Password Management | = | ДА | /предложение/ |
|  | Autoinstall Support for Firmware Images and Configuration Files | = | ДА | /предложение/ |
|  | SNMP v1, v2, and v3 | = | ДА | /предложение/ |
|  | SSH 1.5 and 2.0 | = | ДА | /предложение/ |
|  | SSL 3.0 and TLS 1.0 | = | ДА | /предложение/ |
|  | Secure Copy (SCP) | = | ДА | /предложение/ |
|  | Telnet (Multi-Session Support) | = | ДА | /предложение/ |
| QoS | Access Control Lists (ACLs) Permit/Deny Actions for Inbound IP and Layer 2 Traffic Classification Based on: | Time-Based ACL | = | ДА | /предложение/ |
|  |  | Source/Destination IP Address | = | ДА | /предложение/ |
|  |  | TCP/UDP Source/Destination Port | = | ДА | /предложение/ |
|  |  | IP Protocol Type | = | ДА | /предложение/ |
|  |  | Type of Service (ToS) or Differentiated Services (DSCP) Field | = | ДА | /предложение/ |
|  |  | Source/Destination MAC Address | = | ДА | /предложение/ |
|  |  | EtherType | = | ДА | /предложение/ |
|  |  | IEEE 802.1p User Priority | = | ДА | /предложение/ |
|  |  | VLAN ID | = | ДА | /предложение/ |
|  |  | RFC 1858: Security Considerations for IP Fragment Filtering | = | ДА | /предложение/ |
|  | Optional ACL Rule Attributes | Assign Flow to a Specific Class of Service (CoS) Queue | = | ДА | /предложение/ |
|  |  | Redirect Matching Traffic Flows | = | ДА | /предложение/ |
|  | Differentiated Services (DiffServ) | Classify Traffic Based on Same Criteria as ACLs | = | ДА | /предложение/ |
|  |  | Mark the IP DSCP or Precedence Header Fields, Optional | = | ДА | /предложение/ |
|  |  | Police the Flow to a Specific Rate with Two-Color Aware Support | = | ДА | /предложение/ |
|  |  | RFC 2474: Definition of the Differentiated Services Field (DS field) in the IPv4 and IPv6 Headers | = | ДА | /предложение/ |
|  |  | RFC 2475: An Architecture for Differentiated Services | = | ДА | /предложение/ |
|  |  | RFC 2597: Assured Forwarding Per-Hop Behavior (PHB) Group | = | ДА | /предложение/ |
|  |  | RFC 3246: An Expedited Forwarding PHB | = | ДА | /предложение/ |
|  |  | RFC 3260: New Terminology and Clarifications for DiffServ | = | ДА | /предложение/ |
|  | Class of Service (CoS) Queue Mapping Configuration | AutoVoIP: Automatic CoS Settings for VoIP | = | ДА | /предложение/ |
|  |  | IP DSCP-to-Queue Mapping | = | ДА | /предложение/ |
|  |  | Configurable Interface Trust Mode (IEEE 802.1p, DSCP, or Untrusted) | = | ДА | /предложение/ |
|  |  | Interface Egress Shaping Rate | = | ДА | /предложение/ |
|  |  | Strict Priority versus Weighted Scheduling per Queue | = | ДА | /предложение/ |

3. Мрежов комутатор 3

| Наименование: | Мрежов комутатор 3 |
| --- | --- |
| Марка: | /попълва се от участника/ |
| Модел: | /попълва се от участника/ |
| URL от сайт на производителя: | /попълва се от участника/ |
| Гаранционен срок | >= | 24 месеца | /предложение/ |
| ОСНОВНИ ХАРАКТЕРИСТИКИ | Съвместимост с PacketFence NAC версия 8.1 https://packetfence.org/about.html#/material | = | ДА | /предложение/ |
|  | Rackmount, 1U hight | = | ДА | /предложение/ |
|  | Total Non-Blocking Throughput | >= | 70 Gbps | /предложение/ |
|  | Switching Capacity | >= | 140 Gbps | /предложение/ |
|  | Forwarding Rate | >= | 104,16 Mpps | /предложение/ |
|  | Max. AC Power Consumption | <= | 56 W | /предложение/ |
|  | Power Specs | DC Input Option (Redundant or Stand-Alone) | = | ДА | /предложение/ |
|  |  | AC | 100-240VAC/50-60 Hz, Universal Input | = | ДА | /предложение/ |
|  |  | DC | DC 56W, 25 to 16V, with 2.5 mm DC Power Inline Connector | = | ДА | /предложение/ |
|  |  | Supported Voltage Range | 100 to 240VAC | = | ДА | /предложение/ |
|  |  |  | 25 to 16VDC | = | ДА | /предложение/ |
|  | Interfaces | Networking Interfaces | Total number of ports | >= | 52 | /предложение/ |
|  |  |  | 1/10 Gbps SFP+ Ethernet Ports | >= | 2 | /предложение/ |
|  |  |  | 1 Gbps SFP Ethernet Ports | >= | 2 | /предложение/ |
|  |  |  | 10/100/1000 Mbps RJ45 Ethernet Ports | >= | 48 | /предложение/ |
|  |  | Management Interface | RJ45 Serial Port | >= | 1 | /предложение/ |
|  |  |  | Ethernet In/Out Band | = | ДА | /предложение/ |
|  | Operating Temperature | -5 to 40° C | = | ДА | /предложение/ |
|  | Operating Humidity | 5 to 95% Noncondensing | = | ДА | /предложение/ |
| CORE SWITCHING FEATURES | ANSI/TIA-1057: LLDP-Media Endpoint Discovery (MED) | = | ДА | /предложение/ |
|  | EEE 802.1AB: Link Layer Discovery Protocol (LLDP) | = | ДА | /предложение/ |
|  | EEE 802.1D: Spanning Tree Compatibility | = | ДА | /предложение/ |
|  | IEEE 802.1S: Multiple Spanning Tree Compatibility | = | ДА | /предложение/ |
|  | IEEE 802.1W: Rapid Spanning Tree Compatibility | = | ДА | /предложение/ |
|  | IEEE 802.1Q: Virtual LANs with Port-Based VLANs | = | ДА | /предложение/ |
|  | IEEE 802.1p: Ethernet Priority with User Provisioning and Mapping | = | ДА | /предложение/ |
|  | EEE 802.1X: Port-Based Authentication with Guest VLAN Support | = | ДА | /предложение/ |
|  | EEE 802.3: 10BASE-T | = | ДА | /предложение/ |
|  | IEEE 802.3u: 100BASE-T | = | ДА | /предложение/ |
|  | EEE 802.3ab: 1000BASE-T | = | ДА | /предложение/ |
|  | IEEE 802.1ak: Virtual Bridged Local Area Networks - Amendment 07: Multiple Registration Protocol | = | ДА | /предложение/ |
|  | IEEE 802.3ac: VLAN Tagging | = | ДА | /предложение/ |
|  | IEEE 802.3ad: Link Aggregation | = | ДА | /предложение/ |
|  | IEEE 802.3x: Flow Control | = | ДА | /предложение/ |
|  | IEEE 802.1D-2004: Generic Attribute Registration Protocol: Clause 12 (GARP) | = | ДА | /предложение/ |
|  | IEEE 802.1D-2004: Dynamic L2 multicast registration: Clause 10 (GMRP) | = | ДА | /предложение/ |
|  | IEEE 802.1Q-2003: Dynamic VLAN registration: Clause 11.2 (GVRP) | = | ДА | /предложение/ |
|  | RFC 4541: Considerations for Internet Group Management Protocol (IGMP) Snooping Switches | = | ДА | /предложение/ |
|  | RFC 5171: Unidirectional Link Detection (UDLD) Protocol | = | ДА | /предложение/ |
| ADVANCED LAYER 2 FEATURES | Broadcast Storm Recovery | = | ДА | /предложение/ |
|  | Broadcast/Multicast/Unknown Unicast Storm Recovery | = | ДА | /предложение/ |
|  | DHCP Snooping | = | ДА | /предложение/ |
|  | IGMP Snooping Querier | = | ДА | /предложение/ |
|  | Independent VLAN Learning (IVL) Support | = | ДА | /предложение/ |
|  | Jumbo Ethernet Frame Support | = | ДА | /предложение/ |
|  | Port MAC Locking | = | ДА | /предложение/ |
|  | Port Mirroring | = | ДА | /предложение/ |
|  | Protected Ports | = | ДА | /предложение/ |
|  | Static MAC Filtering | = | ДА | /предложение/ |
|  | TACACS+ | = | ДА | /предложение/ |
|  | Voice VLANs | = | ДА | /предложение/ |
|  | Unauthenticated VLAN | = | ДА | /предложение/ |
|  | Internal 802.1X Authentication Server | = | ДА | /предложение/ |
| PLATFORM SPECIFICATIONS | DHCP Server | Maximum Number of Pools: | >= | 8 | /предложение/ |
|  |  | Maximum Number of Leases (Total): | >= | 128 | /предложение/ |
|  | Routing | Number of Routes: | >= | 16 | /предложение/ |
|  |  | Number of Routing Interfaces: | >= | 15 | /предложение/ |
|  | VLANs: | >= | 255 | /предложение/ |
|  | MAC Addresses: | >= | 8000 | /предложение/ |
|  | MSTP Instances: | >= | 4 | /предложение/ |
|  | LAGs | >= | 6 | /предложение/ |
|  | Traffic Classes (Queues) | >= | 8 | /предложение/ |
| SYSTEM FACILITIES | Event and Error Logging Facility | = | ДА | /предложение/ |
|  | Run-Time and Configuration Download Capability | = | ДА | /предложение/ |
|  | PING Utility | = | ДА | /предложение/ |
|  | FTP/TFTP Transfers via IPv4/IPv6 | = | ДА | /предложение/ |
|  | Malicious Code Detection | = | ДА | /предложение/ |
|  | BootP and DHC | = | ДА | /предложение/ |
|  | RFC 2021: Remote Network Monitoring Management Information Base Version 2 | = | ДА | /предложение/ |
|  | RFC 2030: Simple Network Time Protocol (SNTP | = | ДА | /предложение/ |
|  | RFC 2819: Remote Network Monitoring Management Information Base | = | ДА | /предложение/ |
|  | RFC 2865: RADIUS Client | = | ДА | /предложение/ |
|  | RFC 2866: RADIUS Accounting | = | ДА | /предложение/ |
|  | RFC 2868: RADIUS Attributes for Tunnel Protocol Support | = | ДА | /предложение/ |
|  | RFC 2869: RADIUS Extensions | = | ДА | /предложение/ |
|  | RFC 3579: RADIUS Support for EAP | = | ДА | /предложение/ |
|  | RFC 3580: IEEE 802.1X RADIUS Usage Guidelines | = | ДА | /предложение/ |
|  | RFC 3164: BSD Syslog Protocol | = | ДА | /предложение/ |
| MANAGEMENT | Web UI | = | ДА | /предложение/ |
|  | Industry-Standard CLI | = | ДА | /предложение/ |
|  | IPv6 Management | = | ДА | /предложение/ |
|  | Password Management | = | ДА | /предложение/ |
|  | Autoinstall Support for Firmware Images and Configuration Files | = | ДА | /предложение/ |
|  | SNMP v1, v2, and v3 | = | ДА | /предложение/ |
|  | SSH 1.5 and 2.0 | = | ДА | /предложение/ |
|  | SSL 3.0 and TLS 1.0 | = | ДА | /предложение/ |
|  | Secure Copy (SCP) | = | ДА | /предложение/ |
|  | Telnet (Multi-Session Support) | = | ДА | /предложение/ |
| QoS | Access Control Lists (ACLs) Permit/Deny Actions for Inbound IP and Layer 2 Traffic Classification Based on: | Time-Based ACL | = | ДА | /предложение/ |
|  |  | Source/Destination IP Address | = | ДА | /предложение/ |
|  |  | TCP/UDP Source/Destination Port | = | ДА | /предложение/ |
|  |  | IP Protocol Type | = | ДА | /предложение/ |
|  |  | Type of Service (ToS) or Differentiated Services (DSCP) Field | = | ДА | /предложение/ |
|  |  | Source/Destination MAC Address | = | ДА | /предложение/ |
|  |  | EtherType | = | ДА | /предложение/ |
|  |  | IEEE 802.1p User Priority | = | ДА | /предложение/ |
|  |  | VLAN ID | = | ДА | /предложение/ |
|  |  | RFC 1858: Security Considerations for IP Fragment Filtering | = | ДА | /предложение/ |
|  | Optional ACL Rule Attributes | Assign Flow to a Specific Class of Service (CoS) Queue | = | ДА | /предложение/ |
|  |  | Redirect Matching Traffic Flows | = | ДА | /предложение/ |
|  | Differentiated Services (DiffServ) | Classify Traffic Based on Same Criteria as ACLs | = | ДА | /предложение/ |
|  |  | Mark the IP DSCP or Precedence Header Fields, Optional | = | ДА | /предложение/ |
|  |  | Police the Flow to a Specific Rate with Two-Color Aware Support | = | ДА | /предложение/ |
|  |  | RFC 2474: Definition of the Differentiated Services Field (DS field) in the IPv4 and IPv6 Headers | = | ДА | /предложение/ |
|  |  | RFC 2475: An Architecture for Differentiated Services | = | ДА | /предложение/ |
|  |  | RFC 2597: Assured Forwarding Per-Hop Behavior (PHB) Group | = | ДА | /предложение/ |
|  |  | RFC 3246: An Expedited Forwarding PHB | = | ДА | /предложение/ |
|  |  | RFC 3260: New Terminology and Clarifications for DiffServ | = | ДА | /предложение/ |
|  | Class of Service (CoS) Queue Mapping Configuration | AutoVoIP: Automatic CoS Settings for VoIP | = | ДА | /предложение/ |
|  |  | IP DSCP-to-Queue Mapping | = | ДА | /предложение/ |
|  |  | Configurable Interface Trust Mode (IEEE 802.1p, DSCP, or Untrusted) | = | ДА | /предложение/ |
|  |  | Interface Egress Shaping Rate | = | ДА | /предложение/ |
|  |  | Strict Priority versus Weighted Scheduling per Queue | = | ДА | /предложение/ |

4. Безжична точка за достъп 4

| Наименование: | Безжична точка за достъп 1 |
| --- | --- |
| Марка: | /попълва се от участника/ |
| Модел: | /попълва се от участника/ |
| URL от сайт на производителя: | /попълва се от участника/ |
| Гаранционен срок | >= | 24 месеца | /предложение/ |
| ОСНОВНИ ХАРАКТЕРИСТИКИ | Processor Specs | Atheros MIPS 74Kc, 560 MHz | = | ДА | /предложение/ |
|  | Cross-pol Isolation | 20 dB Minimum | = | ДА | /предложение/ |
|  | Beamwidth | 45° (H-pol) / 45° (V-pol) / 45° (Elevation) | = | ДА | /предложение/ |
|  | Polarization | Dual Linear | = | ДА | /предложение/ |
|  | Enclosure | UV Resistant Polycarbonate | = | ДА | /предложение/ |
|  | Mounting | Pole-Mount (Kit Included) | = | ДА | /предложение/ |
|  | Operating Frequency (MHz) | Worldwide | 5150 – 5875 | = | ДА | /предложение/ |
|  | Management Radio (MHz) | Worldwide | 2412 – 2472 | = | ДА | /предложение/ |
|  | Wi-Fi Standards | 802.11abgn/ac | = | ДА | /предложение/ |
|  | Channel Bandwidths | 10/20/30/40/50/60/80 MHz | = | ДА | /предложение/ |
|  | Antenna Gain | = | 16 dBi | /предложение/ |
|  | Memory DDR2 | >= | 64 MB | /предложение/ |
|  | Power Specs | 24V, 0.5A Gigabit PoE Supply (Included) | = | ДА | /предложение/ |
|  |  | Power Method | 802.3af Alternative A (Pairs 1, 2+; 3, 6 Return) | = | ДА | /предложение/ |
|  |  |  | 24V Passive PoE (Pairs 4, 5+; 7, 8 Return) | = | ДА | /предложение/ |
|  |  | Max. Power Consumption | <= | 8,5W | /предложение/ |
|  | Networking Interfaces | 10/100/1000 Mbps Ethernet Ports | >= | 2 | /предложение/ |
|  | Operating Temperature | -5 to 40° C | = | ДА | /предложение/ |
|  | Operating Humidity | 5 to 95% Noncondensing | = | ДА | /предложение/ |