ПРИЛОЖЕНИЕ

ТЕХНИЧЕСКА СПЕЦИФИКАЦИЯ

Обособена позиция № 1. Офис техника и приложения

1. Компютърна конфигурация № 1 – 2 броя

| Компонент | Харакетристики |
| --- | --- |
| Motherboard | LGA1151, DDR4, PCI-E (HDMI & DVI) (CF), 6x SATA 6Gbps, 5x USB 3.1, ATX |
| CPU | Litography: 14nm # of cores: 6 # of threads: 12 Base Frequency: 3.20 GHz, up to 4.60GHz Cache: 12Mb TDP: 65W |
| RAM | Type: DDR4 Frequency: 2400 MHz, 1.2V Amount: 16GB (2x8GB) |
| Graphics card | PCI-E 3.0 Video Memory: 4GB GDDR5, 128bit Connectors: 1xHDMI, 1xDVI, 1xDisplayPort |
| Storage | 1x SSD, Capacity: 480GB 2x 3.5” 2TB HDD SATA 6Gbps, 7200rpm, 64MB cache |
| Case | Type: ATX, black, 1xUSB3.0 with side glass panel |
| PSU | 700W |
| Гаранционен срок | Не по-малко от 24 месеца |

2. Компютърна конфигурация № 2 – 2 броя

| Компонент | Харакетристики |
| --- | --- |
| Motherboard | 2 free slots available |
| Ports | 6 USB 3.1 Gen 1 (2 front/4 rear) 4 USB 2.0 (2 front/2 rear) 1 front with PowerShare 1 Universal Audio Jack, 1 Line Out LAN: 1xRJ45 port 10/100/1000 Mbits/s 1xSD Card reader |
| CPU | Quad Core CPU, Base Frequency: 3,6GHz, Max Frequency: 4.2 GHz Lithography: 14nm # of cores: 4 # of threads: 8 Cache: 8MB TDP: 65W |
| RAM | 16GB (2x8GB) 2400MHz DDR4 |
| Graphics card | Memory: 4GB, 2xDisplayPort, 1xDVI |
| Storage | 1x 256GB SATA Class 20 |
| CD/DVD | Yes |
| Software | Windows 10 Pro 64bit English |
| Гаранционен срок | Не по-малко от 24 месеца |

3. Компютърна конфигурация № 3 – 1 брой

| Компонент | Харакетристики |
| --- | --- |
| Motherboard | Intel H81 chipset, 2 DIMM slots, supports up to 16GB DDR3) |
| CPU | Litography: 22nm # of cores: 2 # of threads: 4 Base Frequency: 3.60 GHz Cache: 3Mb TDP: 54W |
| RAM | 1x4GB DDR3, 1600MHz |
| Graphics card | Integrated |
| Storage | 1x 3.5” HDD SATA 6Gbps, 500GB, 7200rpm, 64MB cache |
| Build-in Case Audio Speaker | Yes |
| CD/DVD | DVD+/-RW Drive |
| Гаранционен срок | Не по-малко от 24 месеца |

4. Сървърна компютърна конфигурация – 1 брой

| Компонент | Харакетристики |
| --- | --- |
| Motherboard | Chipset: Intel C610, 3xUSB3.0 ports |
| CPU | Litography: 14nm # of cores: 6 # of threads: 6 Base Frequency: 1.70 GHz Cache: 15Mb TDP: 85W |
| RAM | 8GB DDR4 RDIMM DDR4-2133 |
| Storage | 4x3.5” HDD 2TB, 7200rpm |
| Case | Rack |
| PSU | 550W |
| Гаранционен срок | Не по-малко от 24 месеца |

5. Монитор № 1 – 4 броя

| Компонент | Харакетристики |
| --- | --- |
| Panel Type | 24inch IPS |
| Native Resolution | QHD 2560x1440 @ 60Hz |
| Brightness | 350cd/m2 |
| Viewing angle Horizontal/Vertical | 178/178 |
| Contrast ratio | 1000:1 |
| Connectivity | USB 3.0 upstream 2 x USB 3.0 downstream 2 x USB 3.0 downstream with Battery Charging 1.2 DisplayPort Mini DisplayPort HDMI DisplayPort output Audio line-out |
| Гаранционен срок | Не по-малко от 24 месеца |

6. Монитор № 2 – 1 брой

| Компонент | Харакетристики |
| --- | --- |
| Panel Type | 21 inch A-Si TFT Active Matrix LCD |
| Native Resolution | 1920x1080 |
| Aspect | 16:9 |
| Viewing angle Horizontal/Vertical | 170/160 hotizontal/vertical |
| Option in connector | D-sub 9-pin (x1), female |
| RGB, Component | BNC (x3), loop-through, with 75 ohms automatic termination |
| Power requirements | AC 100 V to 240 V, 50/60 Hz |
| Гаранционен срок | Не по-малко от 24 месеца |

7. Преносим компютър № 1 – 2 броя

| Компонент | Харакетристики |
| --- | --- |
| Screen Sice | 15.6 inch Full HD |
| CPU | Litography: 14nm # of cores: 2 # of threads: 4 Base Frequency: 2.50 GHz, up to 3.10GHz Cache: 4Mb TDP: 15W |
| RAM | Type: DDR3L Amount: 8GB |
| Graphics card | Video Memory: 2GB GDDR3 Connectors: 1xHDMI, 1xDVI, 1xDisplayPort |
| Storage | 1x 1TB HDD SATA 6Gbps |
| USB ports | 2xUSB 3.0 |
| OS | Windows 10 Home |
| Гаранционен срок | Не по-малко от 24 месеца |

8. Преносим компютър № 2 – 2 броя

| Компонент | Харакетристики |
| --- | --- |
| Screen Size | 13.3 inch Full HD |
| CPU | Litography: 14nm # of cores: 2 # of threads: 4 Base Frequency: 2.30 GHz Cache: 3Mb TDP: 15W |
| RAM | Type: DDR4, 2133MHz Amount: 12GB (1x4096MB + 1x8192MB) |
| Graphics card | Built-in graphics adapter |
| Storage | 1x 1TB HDD SATA 6Gbps |
| Network Connectivity | LAN 10/100/1000 mb/sec. Wi-Fi 802.11a/b/g/n, 3G/UMTS GOBI 3000, Bluetooth 4.0; |
| Camera | Integrated HD Webcam with microphone |
| Гаранционен срок | Не по-малко от 24 месеца |

9. Принтер – 1 брой

| Компонент | Харакетристики |
| --- | --- |
| Разделителна способност | Up to 9600x2400 dpi |
| Система за печат | Мастиленоструйна технология с FINE печатаща глава 5-цветна система с мин. размер на мастилената капка 1 pl |
| Скорост на печат на монохромен документ | ESAT: приблиз. 15,0 ipm |
| Скорост на печат на цветен документ | ESAT: приблиз. 10,0 ipm |
| Печат без бели полета | Да (формат A4, Letter, 20x25 cm, 13х18 cm и 10x15 cm) |
| Скорост на фотопечат | Без бели полета 10x15cm: приблиз. 21 s |
| Двустранен печат | Автоматичен двустранен печат (A4, A5, B5, Letter) |
| Директен печат върху диск | Да (включен софтуер) |
| Други финкции за печат | Печат с вместване в страницата, Печат с мащабиране, Печат на няколко страници върху един лист, Печат на брошура, Печат на постер |
| Капацитет на патрона с мастило - печат на документи | Цветен документ A4 Пигментно черно: 300 стр. Пигментно черно XL: 500 стр. Черно: 1795 стр. Черно XL: 5530* стр. Циан: 332 страници Циан XL: 695 стр. Магента: 319 стр. Магента XL: 680 стр. Жълто: 344 стр. Жълто XL: 695 стр. |
| Капацитет на патрона с мастило - печат на снимки | Снимка с размер 10x15 cm Пигментно черно: 2425 снимки Пигментно черно XL: 5615 снимки Черно: 376 снимки Черно XL: 1130 снимки Циан: 121 снимки Циан XL: 267 снимки Магента: 132 снимки Магента XL: 313 снимки Жълто: 130 снимки Жълто XL: 274 снимки |
| Типове хартия | Обикновена хартия, Пликове, Photo Paper Pro Platinum (PT-101), Photo Paper Plus Glossy II (PP-201), Photo Paper Pro Luster (LU-101), Photo Paper Plus Semi-gloss (SG-201), Glossy Photo Paper "За всекидневна употреба" (GP-501), Matte Photo Paper (MP-101), High Resolution Paper (HR-101N), T-shirt Transfer (TR-301), Photo Stickers (PS-101) |
| Максимален капацитет за зареждане с хартия | Долна касета: макс. 125 листа (обикновена хартия) Горна касета: макс. 20 листа (фотохартия) Тава за директен печат върху диск: 1 печатаем CD, DVD или Blu-Ray диск |
| Интерфейс | Hi-Speed USB (порт B) Wi-Fi: IEEE802.11 b/g/n Wi-Fi сигурност: WPA-PSK, WPA2-PSK, WEP Честотна лента на безжична LAN: 2,4 GHz |
| Поддържани операционни системи | Windows 10 (32 и 64 бита) Windows 8 (32 и 64bit) Windows RT Windows 7 (32 и 64 bit) Windows Vista SP1, SP2 (32 и 64 bit) Windows XP SP3 (32 bit) Mac OS X |
| Гаранционен срок | Не по-малко от 24 месеца |

10. Мобилни устройства – Таблет – 2 броя

| Компонент | Харакетристики |
| --- | --- |
| Тегло | 430 г |
| Размери | 240.5 x 163.7 x 7.2 mm |
| OS | Android 7 Nougat |
| Screen Size | 9.7 inch |
| Resolution | 1536 x 2048 |
| CPU | Hexa-core, CortexA72 + CortexA53 |
| RAM | 4GB |
| Storage | 32GB |
| Camera | 8MP |
| Гаранционен срок | Не по-малко от 24 месеца |

11. UPS – 1 брой

| Компонент | Харакетристики |
| --- | --- |
| Входна мощност (VA) | 1500 VA |
| Изходна мощност | 865 W |
| Рейтинг на пренапрежение | 445 J |
| Технология на батерията | Sealed Lead Acid (VRLA) |
| Време за зареждане на батерия | 8h |
| Нормално време за бекъп при 50% натоварване | 20.9 min |
| Нормално време за бекъп при 100% натоварване | 7.6 min |
| Картридж с резервни батерии | RBC59 |
| Изходни конектори | (4) IEC 320 C13 \n(2) IEC Jumpers |
| Тип на входните конектори | IEC-320 C14 |
| Номинално изходно напрежение | 230V |
| Филтриране | 5% IEEE/UL 1449 |
| Номинално входно напрежение | 230V |
| Гаранционен срок | Не по-малко от 24 месеца |

12. Софтуерни продукти

| № | Продукт | Описание | Количество |
| --- | --- | --- | --- |
| 1 | OfficeProPlus 2013 SNGL OLP NL | Софтуерът включвa: Word, Excel, Power Point, Outlook, OneNote, Publisher, Access, InfoPath, SharePoint Workspace, Lync | 1 |
| 2. | CUBASE 8,5PRO, CUBASE |  | 1 |
| 3. | WAVELAB 8,5 |  | 1 |
| 4 | ADOBE PREMIERE PRO/CLOUD MONTH SUBSCRIPTION |  | 1 |

Обособена позиция № 2. Аудио-визуална техника

1. Мултимедиен прожектор – 1 брой

| Компонент | Харакетристики |
| --- | --- |
| Lumens | 5000 ANSI Lumens |
| Contrast Ratio | 20,000:1 |
| Formats | 4:3 (Native), 16:9 (Supported) Noise, dB 33 dBA (Standard),28 dBA (ECO) |
| Digital Zoom | 2x |
| Connectors | HDMIx1, USBx1(mini-B), Composite Video, Component Video, S-Video, RJ-45, VGA-In, VGA-Out, Audio-In, Audio-Out |
| Lamp | UHP, 310W |
| Lamp Life | Normal Mode – 3000 Hour Economy Mode – 4000 Hour Extreme Eco Mode – 4500 Hour |
| Lens | Projection lens: F = 2.50 ~ 2.93, f = 15.98mm ~ 21.42mm, = Manual Zoom & Focus; Throw ratio: 1.40 ~ 1.91 (70"@2m) |
| Гаранционен срок | Не по-малко от 24 месеца |

2. Интерактивен дисплей – 1 брой

| Компонент | Харакетристики |
| --- | --- |
| Panel Type | ≥ 84" class (84" diagonal) ultra HD multi-touch signage, Brilliant HD 1920x1080 |
| Display type | UV2A LED дисплей |
| Size | 300 nit Display - 16/7 Operation; 3840 x 2160 (Ultra HD) |
| Multi Touch | ≥ 10-point capacitive multi-touch screen with edge to edge glass; |
| Muti User | До 4 едновременно работещи потребители |
| Technology | Infrared Touch |
| Audio | Вградена 10W канална стерео аудио система; |
| UHD Support | Yes |
| Protective Glass | Anti-Fog, Anti-Glass |
| USB Playback | Yes |

3. Аксесоари за интерактивна дисплей система

| Компонент | Характеристики |
| --- | --- |
| Презентер – 1 брой | Безжичен презентер; 30 метров ефективен диапазон с 2.4 GHz безжична технология; LCD дисплей с таймер и индикатор; Бутони за слайдшоу, бутон за включване / изключване; Без софтуерна инсталация. Размери: 4.1х22.2х17 см |
| Интерактивен кит за проектори – 1 брой | Площ: ≥120"; 4 потребители; Автоматична калибрация, запис, ≥USB 2.0 |
| Гаранционен срок | Не по-малко от 24 месеца |

4. Електрически екран за проектор – 1 брой

| Компонент | Харакетристики |
| --- | --- |
| Диагонал на картината | 100” |
| Размер на картината ш/в | 203.2x152.4см |
| Aspect Ratio | 4:3 |
| Платно | бяло |
| Кутия д/в/ш в см | 236.6/8.0/9.3 |
| Горна черна лента | Да |
| Гаранционен срок | Не по-малко от 24 месеца |

5. Преносима маса (стойка) за проектор – 1 брой

| Компонент | Харакетристики |
| --- | --- |
| Товароносимост | До 30кг |
| Регулируема височина | 80-125см |
| Механизъм | 4 колела с блокировка |
| Поставка | 50х40см |
| Наклон | 15о |
| Материал | Стомана |

6. Стойка за проектор – 1 брой

| Компонент | Харакетристики |
| --- | --- |
| Тип | Стойка за таван |

7. Стойка за интерактивен дисплей – 1 брой

| Компонент | Харакетристики |
| --- | --- |
| Тип | Стойка за таван |

8. Тонколони - 1 комплект

| Компонент | Харакетристики |
| --- | --- |
| Total Watts (RMS) | 500 |
| Subwoofer Watts | 165 |
| Satellites | 5 x 67W |
| THX Certified | Yes |
| DTS Decodind | Yes |
| 3D Stereo | Yes |
| Digital optical inputs | 2 |
| Digital coaxial inputs | 1 |
| Six channel direct input | Yes |
| Satellite Wall mounting | Yes |
| Гаранционен срок | Не по-малко от 24 месеца |

Обособена позиция № 3. Мрежово оборудване

1. Мрежови комутатор 1

| Наименование: | Мрежов комутатор 1 |
| --- | --- |
| Прогнозно количество за една година: | 2 броя |
| Гаранционен срок | >= | 24 месеца |
| ОСНОВНИ ХАРАКТЕРИСТИКИ | Съвместимост с PacketFence NAC версия 8.1 https://packetfence.org/about.html#/material | = | ДА |
|  | Rackmount, 1U hight | = | ДА |
|  | Total Non-Blocking Throughput | >= | 16 Gbps |
|  | Switching Capacity | >= | 32 Gbps |
|  | Forwarding Rate | >= | 23,81 Mpps |
|  | Max. AC Power Consumption | <= | 56 W |
|  | Power Specs | DC Input Option (Redundant or Stand-Alone) | = | ДА |
|  |  | AC | 100-240VAC/50-60 Hz, Universal Input | = | ДА |
|  |  | DC | DC 56W, 25 to 16V, with 2.5 mm DC Power Inline Connector | = | ДА |
|  |  | Supported Voltage Range | 100 to 240VAC | = | ДА |
|  |  |  | 25 to 16VDC | = | ДА |
|  | Interfaces | Networking Interfaces | Total number of ports | >= | 16 |
|  |  |  | 100/1000 Mbps SFP Ethernet Ports | >= | 8 |
|  |  |  | 1000 Mbps SFP Ethernet Ports | >= | 4 |
|  |  |  | 10/100/1000 Mbps RJ45 Ethernet Ports | >= | 4 |
|  |  | Management Interface | RJ45 Serial Port | >= | 1 |
|  |  |  | Ethernet In/Out Band | = | ДА |
|  | Operating Temperature | -5 to 40° C | = | ДА |
|  | Operating Humidity | 5 to 95% Noncondensing | = | ДА |
| CORE SWITCHING FEATURES | ANSI/TIA-1057: LLDP-Media Endpoint Discovery (MED) | = | ДА |
|  | EEE 802.1AB: Link Layer Discovery Protocol (LLDP) | = | ДА |
|  | EEE 802.1D: Spanning Tree Compatibility | = | ДА |
|  | IEEE 802.1S: Multiple Spanning Tree Compatibility | = | ДА |
|  | IEEE 802.1W: Rapid Spanning Tree Compatibility | = | ДА |
|  | IEEE 802.1Q: Virtual LANs with Port-Based VLANs | = | ДА |
|  | IEEE 802.1p: Ethernet Priority with User Provisioning and Mapping | = | ДА |
|  | EEE 802.1X: Port-Based Authentication with Guest VLAN Support | = | ДА |
|  | EEE 802.3: 10BASE-T | = | ДА |
|  | IEEE 802.3u: 100BASE-T | = | ДА |
|  | EEE 802.3ab: 1000BASE-T | = | ДА |
|  | IEEE 802.1ak: Virtual Bridged Local Area Networks - Amendment 07: Multiple Registration Protocol | = | ДА |
|  | IEEE 802.3ac: VLAN Tagging | = | ДА |
|  | IEEE 802.3ad: Link Aggregation | = | ДА |
|  | IEEE 802.3x: Flow Control | = | ДА |
|  | IEEE 802.1D-2004: Generic Attribute Registration Protocol: Clause 12 (GARP) | = | ДА |
|  | IEEE 802.1D-2004: Dynamic L2 multicast registration: Clause 10 (GMRP) | = | ДА |
|  | IEEE 802.1Q-2003: Dynamic VLAN registration: Clause 11.2 (GVRP) | = | ДА |
|  | RFC 4541: Considerations for Internet Group Management Protocol (IGMP) Snooping Switches | = | ДА |
|  | RFC 5171: Unidirectional Link Detection (UDLD) Protocol | = | ДА |
| ADVANCED LAYER 2 FEATURES | Broadcast Storm Recovery | = | ДА |
|  | Broadcast/Multicast/Unknown Unicast Storm Recovery | = | ДА |
|  | DHCP Snooping | = | ДА |
|  | IGMP Snooping Querier | = | ДА |
|  | Independent VLAN Learning (IVL) Support | = | ДА |
|  | Jumbo Ethernet Frame Support | = | ДА |
|  | Port MAC Locking | = | ДА |
|  | Port Mirroring | = | ДА |
|  | Protected Ports | = | ДА |
|  | Static MAC Filtering | = | ДА |
|  | TACACS+ | = | ДА |
|  | Voice VLANs | = | ДА |
|  | Unauthenticated VLAN | = | ДА |
|  | Internal 802.1X Authentication Server | = | ДА |
| PLATFORM SPECIFICATIONS | DHCP Server | Maximum Number of Pools: | >= | 8 |
|  |  | Maximum Number of Leases (Total): | >= | 128 |
|  | Routing | Number of Routes: | >= | 16 |
|  |  | Number of Routing Interfaces: | >= | 15 |
|  | VLANs: | >= | 255 |
|  | MAC Addresses: | >= | 8000 |
|  | MSTP Instances: | >= | 4 |
|  | LAGs | >= | 6 |
|  | Traffic Classes (Queues) | >= | 8 |
| SYSTEM FACILITIES | Event and Error Logging Facility | = | ДА |
|  | Run-Time and Configuration Download Capability | = | ДА |
|  | PING Utility | = | ДА |
|  | FTP/TFTP Transfers via IPv4/IPv6 | = | ДА |
|  | Malicious Code Detection | = | ДА |
|  | BootP and DHC | = | ДА |
|  | RFC 2021: Remote Network Monitoring Management Information Base Version 2 | = | ДА |
|  | RFC 2030: Simple Network Time Protocol (SNTP | = | ДА |
|  | RFC 2819: Remote Network Monitoring Management Information Base | = | ДА |
|  | RFC 2865: RADIUS Client | = | ДА |
|  | RFC 2866: RADIUS Accounting | = | ДА |
|  | RFC 2868: RADIUS Attributes for Tunnel Protocol Support | = | ДА |
|  | RFC 2869: RADIUS Extensions | = | ДА |
|  | RFC 3579: RADIUS Support for EAP | = | ДА |
|  | RFC 3580: IEEE 802.1X RADIUS Usage Guidelines | = | ДА |
|  | RFC 3164: BSD Syslog Protocol | = | ДА |
| MANAGEMENT | Web UI | = | ДА |
|  | Industry-Standard CLI | = | ДА |
|  | IPv6 Management | = | ДА |
|  | Password Management | = | ДА |
|  | Autoinstall Support for Firmware Images and Configuration Files | = | ДА |
|  | SNMP v1, v2, and v3 | = | ДА |
|  | SSH 1.5 and 2.0 | = | ДА |
|  | SSL 3.0 and TLS 1.0 | = | ДА |
|  | Secure Copy (SCP) | = | ДА |
|  | Telnet (Multi-Session Support) | = | ДА |
| QoS | Access Control Lists (ACLs) Permit/Deny Actions for Inbound IP and Layer 2 Traffic Classification Based on: | Time-Based ACL | = | ДА |
|  |  | Source/Destination IP Address | = | ДА |
|  |  | TCP/UDP Source/Destination Port | = | ДА |
|  |  | IP Protocol Type | = | ДА |
|  |  | Type of Service (ToS) or Differentiated Services (DSCP) Field | = | ДА |
|  |  | Source/Destination MAC Address | = | ДА |
|  |  | EtherType | = | ДА |
|  |  | IEEE 802.1p User Priority | = | ДА |
|  |  | VLAN ID | = | ДА |
|  |  | RFC 1858: Security Considerations for IP Fragment Filtering | = | ДА |
|  | Optional ACL Rule Attributes | Assign Flow to a Specific Class of Service (CoS) Queue | = | ДА |
|  |  | Redirect Matching Traffic Flows | = | ДА |
|  | Differentiated Services (DiffServ) | Classify Traffic Based on Same Criteria as ACLs | = | ДА |
|  |  | Mark the IP DSCP or Precedence Header Fields, Optional | = | ДА |
|  |  | Police the Flow to a Specific Rate with Two-Color Aware Support | = | ДА |
|  |  | RFC 2474: Definition of the Differentiated Services Field (DS field) in the IPv4 and IPv6 Headers | = | ДА |
|  |  | RFC 2475: An Architecture for Differentiated Services | = | ДА |
|  |  | RFC 2597: Assured Forwarding Per-Hop Behavior (PHB) Group | = | ДА |
|  |  | RFC 3246: An Expedited Forwarding PHB | = | ДА |
|  |  | RFC 3260: New Terminology and Clarifications for DiffServ | = | ДА |
|  | Class of Service (CoS) Queue Mapping Configuration | AutoVoIP: Automatic CoS Settings for VoIP | = | ДА |
|  |  | IP DSCP-to-Queue Mapping | = | ДА |
|  |  | Configurable Interface Trust Mode (IEEE 802.1p, DSCP, or Untrusted) | = | ДА |
|  |  | Interface Egress Shaping Rate | = | ДА |
|  |  | Strict Priority versus Weighted Scheduling per Queue | = | ДА |

2. Мрежови комутатор 2

| Наименование: | Мрежов комутатор 2 |
| --- | --- |
| Прогнозно количество за една година: | 10 броя |
| Гаранционен срок | >= | 24 месеца |
| ОСНОВНИ ХАРАКТЕРИСТИКИ | Съвместимост с PacketFence NAC версия 8.1 https://packetfence.org/about.html#/material | = | ДА |
|  | Rackmount, 1U hight | = | ДА |
|  | Total Non-Blocking Throughput | >= | 26 Gbps |
|  | Switching Capacity | >= | 52 Gbps |
|  | Forwarding Rate | >= | 38,69 Mpps |
|  | Max. AC Power Consumption | <= | 25 W |
|  | Power Specs | DC Input Option (Redundant or Stand-Alone) | = | ДА |
|  |  | AC | 100-240VAC/50-60 Hz, Universal Input | = | ДА |
|  |  | DC | DC 56W, 25 to 16V, with 2.5 mm DC Power Inline Connector | = | ДА |
|  |  | Supported Voltage Range | 100 to 240VAC | = | ДА |
|  |  |  | 25 to 16VDC | = | ДА |
|  | Interfaces | Networking Interfaces | Total number of ports | >= | 26 |
|  |  |  | 1 Gbps SFP Ethernet Ports | >= | 2 |
|  |  |  | 10/100/1000 Mbps RJ45 Ethernet Ports | >= | 24 |
|  |  | Management Interface | RJ45 Serial Port | >= | 1 |
|  |  |  | Ethernet In/Out Band | = | ДА |
|  | Operating Temperature | -5 to 40° C | = | ДА |
|  | Operating Humidity | 5 to 95% Noncondensing | = | ДА |
| CORE SWITCHING FEATURES | ANSI/TIA-1057: LLDP-Media Endpoint Discovery (MED) | = | ДА |
|  | EEE 802.1AB: Link Layer Discovery Protocol (LLDP) | = | ДА |
|  | EEE 802.1D: Spanning Tree Compatibility | = | ДА |
|  | IEEE 802.1S: Multiple Spanning Tree Compatibility | = | ДА |
|  | IEEE 802.1W: Rapid Spanning Tree Compatibility | = | ДА |
|  | IEEE 802.1Q: Virtual LANs with Port-Based VLANs | = | ДА |
|  | IEEE 802.1p: Ethernet Priority with User Provisioning and Mapping | = | ДА |
|  | EEE 802.1X: Port-Based Authentication with Guest VLAN Support | = | ДА |
|  | EEE 802.3: 10BASE-T | = | ДА |
|  | IEEE 802.3u: 100BASE-T | = | ДА |
|  | EEE 802.3ab: 1000BASE-T | = | ДА |
|  | IEEE 802.1ak: Virtual Bridged Local Area Networks - Amendment 07: Multiple Registration Protocol | = | ДА |
|  | IEEE 802.3ac: VLAN Tagging | = | ДА |
|  | IEEE 802.3ad: Link Aggregation | = | ДА |
|  | IEEE 802.3x: Flow Control | = | ДА |
|  | IEEE 802.1D-2004: Generic Attribute Registration Protocol: Clause 12 (GARP) | = | ДА |
|  | IEEE 802.1D-2004: Dynamic L2 multicast registration: Clause 10 (GMRP) | = | ДА |
|  | IEEE 802.1Q-2003: Dynamic VLAN registration: Clause 11.2 (GVRP) | = | ДА |
|  | RFC 4541: Considerations for Internet Group Management Protocol (IGMP) Snooping Switches | = | ДА |
|  | RFC 5171: Unidirectional Link Detection (UDLD) Protocol | = | ДА |
| ADVANCED LAYER 2 FEATURES | Broadcast Storm Recovery | = | ДА |
|  | Broadcast/Multicast/Unknown Unicast Storm Recovery | = | ДА |
|  | DHCP Snooping | = | ДА |
|  | IGMP Snooping Querier | = | ДА |
|  | Independent VLAN Learning (IVL) Support | = | ДА |
|  | Jumbo Ethernet Frame Support | = | ДА |
|  | Port MAC Locking | = | ДА |
|  | Port Mirroring | = | ДА |
|  | Protected Ports | = | ДА |
|  | Static MAC Filtering | = | ДА |
|  | TACACS+ | = | ДА |
|  | Voice VLANs | = | ДА |
|  | Unauthenticated VLAN | = | ДА |
|  | Internal 802.1X Authentication Server | = | ДА |
| PLATFORM SPECIFICATIONS | DHCP Server | Maximum Number of Pools: | >= | 8 |
|  |  | Maximum Number of Leases (Total): | >= | 128 |
|  | Routing | Number of Routes: | >= | 16 |
|  |  | Number of Routing Interfaces: | >= | 15 |
|  | VLANs: | >= | 255 |
|  | MAC Addresses: | >= | 8000 |
|  | MSTP Instances: | >= | 4 |
|  | LAGs | >= | 6 |
|  | Traffic Classes (Queues) | >= | 8 |
| SYSTEM FACILITIES | Event and Error Logging Facility | = | ДА |
|  | Run-Time and Configuration Download Capability | = | ДА |
|  | PING Utility | = | ДА |
|  | FTP/TFTP Transfers via IPv4/IPv6 | = | ДА |
|  | Malicious Code Detection | = | ДА |
|  | BootP and DHC | = | ДА |
|  | RFC 2021: Remote Network Monitoring Management Information Base Version 2 | = | ДА |
|  | RFC 2030: Simple Network Time Protocol (SNTP | = | ДА |
|  | RFC 2819: Remote Network Monitoring Management Information Base | = | ДА |
|  | RFC 2865: RADIUS Client | = | ДА |
|  | RFC 2866: RADIUS Accounting | = | ДА |
|  | RFC 2868: RADIUS Attributes for Tunnel Protocol Support | = | ДА |
|  | RFC 2869: RADIUS Extensions | = | ДА |
|  | RFC 3579: RADIUS Support for EAP | = | ДА |
|  | RFC 3580: IEEE 802.1X RADIUS Usage Guidelines | = | ДА |
|  | RFC 3164: BSD Syslog Protocol | = | ДА |
| MANAGEMENT | Web UI | = | ДА |
|  | Industry-Standard CLI | = | ДА |
|  | IPv6 Management | = | ДА |
|  | Password Management | = | ДА |
|  | Autoinstall Support for Firmware Images and Configuration Files | = | ДА |
|  | SNMP v1, v2, and v3 | = | ДА |
|  | SSH 1.5 and 2.0 | = | ДА |
|  | SSL 3.0 and TLS 1.0 | = | ДА |
|  | Secure Copy (SCP) | = | ДА |
|  | Telnet (Multi-Session Support) | = | ДА |
| QoS | Access Control Lists (ACLs) Permit/Deny Actions for Inbound IP and Layer 2 Traffic Classification Based on: | Time-Based ACL | = | ДА |
|  |  | Source/Destination IP Address | = | ДА |
|  |  | TCP/UDP Source/Destination Port | = | ДА |
|  |  | IP Protocol Type | = | ДА |
|  |  | Type of Service (ToS) or Differentiated Services (DSCP) Field | = | ДА |
|  |  | Source/Destination MAC Address | = | ДА |
|  |  | EtherType | = | ДА |
|  |  | IEEE 802.1p User Priority | = | ДА |
|  |  | VLAN ID | = | ДА |
|  |  | RFC 1858: Security Considerations for IP Fragment Filtering | = | ДА |
|  | Optional ACL Rule Attributes | Assign Flow to a Specific Class of Service (CoS) Queue | = | ДА |
|  |  | Redirect Matching Traffic Flows | = | ДА |
|  | Differentiated Services (DiffServ) | Classify Traffic Based on Same Criteria as ACLs | = | ДА |
|  |  | Mark the IP DSCP or Precedence Header Fields, Optional | = | ДА |
|  |  | Police the Flow to a Specific Rate with Two-Color Aware Support | = | ДА |
|  |  | RFC 2474: Definition of the Differentiated Services Field (DS field) in the IPv4 and IPv6 Headers | = | ДА |
|  |  | RFC 2475: An Architecture for Differentiated Services | = | ДА |
|  |  | RFC 2597: Assured Forwarding Per-Hop Behavior (PHB) Group | = | ДА |
|  |  | RFC 3246: An Expedited Forwarding PHB | = | ДА |
|  |  | RFC 3260: New Terminology and Clarifications for DiffServ | = | ДА |
|  | Class of Service (CoS) Queue Mapping Configuration | AutoVoIP: Automatic CoS Settings for VoIP | = | ДА |
|  |  | IP DSCP-to-Queue Mapping | = | ДА |
|  |  | Configurable Interface Trust Mode (IEEE 802.1p, DSCP, or Untrusted) | = | ДА |
|  |  | Interface Egress Shaping Rate | = | ДА |
|  |  | Strict Priority versus Weighted Scheduling per Queue | = | ДА |

3. Мрежови комутатор 3

| Наименование: | Мрежов комутатор 3 |
| --- | --- |
| Прогнозно количество за една година: | 10 броя |
| Гаранционен срок | >= | 24 месеца |
| ОСНОВНИ ХАРАКТЕРИСТИКИ | Съвместимост с PacketFence NAC версия 8.1 https://packetfence.org/about.html#/material | = | ДА |
|  | Rackmount, 1U hight | = | ДА |
|  | Total Non-Blocking Throughput | >= | 70 Gbps |
|  | Switching Capacity | >= | 140 Gbps |
|  | Forwarding Rate | >= | 104,16 Mpps |
|  | Max. AC Power Consumption | <= | 56 W |
|  | Power Specs | DC Input Option (Redundant or Stand-Alone) | = | ДА |
|  |  | AC | 100-240VAC/50-60 Hz, Universal Input | = | ДА |
|  |  | DC | DC 56W, 25 to 16V, with 2.5 mm DC Power Inline Connector | = | ДА |
|  |  | Supported Voltage Range | 100 to 240VAC | = | ДА |
|  |  |  | 25 to 16VDC | = | ДА |
|  | Interfaces | Networking Interfaces | Total number of ports | >= | 52 |
|  |  |  | 1/10 Gbps SFP+ Ethernet Ports | >= | 2 |
|  |  |  | 1 Gbps SFP Ethernet Ports | >= | 2 |
|  |  |  | 10/100/1000 Mbps RJ45 Ethernet Ports | >= | 48 |
|  |  | Management Interface | RJ45 Serial Port | >= | 1 |
|  |  |  | Ethernet In/Out Band | = | ДА |
|  | Operating Temperature | -5 to 40° C | = | ДА |
|  | Operating Humidity | 5 to 95% Noncondensing | = | ДА |
| CORE SWITCHING FEATURES | ANSI/TIA-1057: LLDP-Media Endpoint Discovery (MED) | = | ДА |
|  | EEE 802.1AB: Link Layer Discovery Protocol (LLDP) | = | ДА |
|  | EEE 802.1D: Spanning Tree Compatibility | = | ДА |
|  | IEEE 802.1S: Multiple Spanning Tree Compatibility | = | ДА |
|  | IEEE 802.1W: Rapid Spanning Tree Compatibility | = | ДА |
|  | IEEE 802.1Q: Virtual LANs with Port-Based VLANs | = | ДА |
|  | IEEE 802.1p: Ethernet Priority with User Provisioning and Mapping | = | ДА |
|  | EEE 802.1X: Port-Based Authentication with Guest VLAN Support | = | ДА |
|  | EEE 802.3: 10BASE-T | = | ДА |
|  | IEEE 802.3u: 100BASE-T | = | ДА |
|  | EEE 802.3ab: 1000BASE-T | = | ДА |
|  | IEEE 802.1ak: Virtual Bridged Local Area Networks - Amendment 07: Multiple Registration Protocol | = | ДА |
|  | IEEE 802.3ac: VLAN Tagging | = | ДА |
|  | IEEE 802.3ad: Link Aggregation | = | ДА |
|  | IEEE 802.3x: Flow Control | = | ДА |
|  | IEEE 802.1D-2004: Generic Attribute Registration Protocol: Clause 12 (GARP) | = | ДА |
|  | IEEE 802.1D-2004: Dynamic L2 multicast registration: Clause 10 (GMRP) | = | ДА |
|  | IEEE 802.1Q-2003: Dynamic VLAN registration: Clause 11.2 (GVRP) | = | ДА |
|  | RFC 4541: Considerations for Internet Group Management Protocol (IGMP) Snooping Switches | = | ДА |
|  | RFC 5171: Unidirectional Link Detection (UDLD) Protocol | = | ДА |
| ADVANCED LAYER 2 FEATURES | Broadcast Storm Recovery | = | ДА |
|  | Broadcast/Multicast/Unknown Unicast Storm Recovery | = | ДА |
|  | DHCP Snooping | = | ДА |
|  | IGMP Snooping Querier | = | ДА |
|  | Independent VLAN Learning (IVL) Support | = | ДА |
|  | Jumbo Ethernet Frame Support | = | ДА |
|  | Port MAC Locking | = | ДА |
|  | Port Mirroring | = | ДА |
|  | Protected Ports | = | ДА |
|  | Static MAC Filtering | = | ДА |
|  | TACACS+ | = | ДА |
|  | Voice VLANs | = | ДА |
|  | Unauthenticated VLAN | = | ДА |
|  | Internal 802.1X Authentication Server | = | ДА |
| PLATFORM SPECIFICATIONS | DHCP Server | Maximum Number of Pools: | >= | 8 |
|  |  | Maximum Number of Leases (Total): | >= | 128 |
|  | Routing | Number of Routes: | >= | 16 |
|  |  | Number of Routing Interfaces: | >= | 15 |
|  | VLANs: | >= | 255 |
|  | MAC Addresses: | >= | 8000 |
|  | MSTP Instances: | >= | 4 |
|  | LAGs | >= | 6 |
|  | Traffic Classes (Queues) | >= | 8 |
| SYSTEM FACILITIES | Event and Error Logging Facility | = | ДА |
|  | Run-Time and Configuration Download Capability | = | ДА |
|  | PING Utility | = | ДА |
|  | FTP/TFTP Transfers via IPv4/IPv6 | = | ДА |
|  | Malicious Code Detection | = | ДА |
|  | BootP and DHC | = | ДА |
|  | RFC 2021: Remote Network Monitoring Management Information Base Version 2 | = | ДА |
|  | RFC 2030: Simple Network Time Protocol (SNTP | = | ДА |
|  | RFC 2819: Remote Network Monitoring Management Information Base | = | ДА |
|  | RFC 2865: RADIUS Client | = | ДА |
|  | RFC 2866: RADIUS Accounting | = | ДА |
|  | RFC 2868: RADIUS Attributes for Tunnel Protocol Support | = | ДА |
|  | RFC 2869: RADIUS Extensions | = | ДА |
|  | RFC 3579: RADIUS Support for EAP | = | ДА |
|  | RFC 3580: IEEE 802.1X RADIUS Usage Guidelines | = | ДА |
|  | RFC 3164: BSD Syslog Protocol | = | ДА |
| MANAGEMENT | Web UI | = | ДА |
|  | Industry-Standard CLI | = | ДА |
|  | IPv6 Management | = | ДА |
|  | Password Management | = | ДА |
|  | Autoinstall Support for Firmware Images and Configuration Files | = | ДА |
|  | SNMP v1, v2, and v3 | = | ДА |
|  | SSH 1.5 and 2.0 | = | ДА |
|  | SSL 3.0 and TLS 1.0 | = | ДА |
|  | Secure Copy (SCP) | = | ДА |
|  | Telnet (Multi-Session Support) | = | ДА |
| QoS | Access Control Lists (ACLs) Permit/Deny Actions for Inbound IP and Layer 2 Traffic Classification Based on: | Time-Based ACL | = | ДА |
|  |  | Source/Destination IP Address | = | ДА |
|  |  | TCP/UDP Source/Destination Port | = | ДА |
|  |  | IP Protocol Type | = | ДА |
|  |  | Type of Service (ToS) or Differentiated Services (DSCP) Field | = | ДА |
|  |  | Source/Destination MAC Address | = | ДА |
|  |  | EtherType | = | ДА |
|  |  | IEEE 802.1p User Priority | = | ДА |
|  |  | VLAN ID | = | ДА |
|  |  | RFC 1858: Security Considerations for IP Fragment Filtering | = | ДА |
|  | Optional ACL Rule Attributes | Assign Flow to a Specific Class of Service (CoS) Queue | = | ДА |
|  |  | Redirect Matching Traffic Flows | = | ДА |
|  | Differentiated Services (DiffServ) | Classify Traffic Based on Same Criteria as ACLs | = | ДА |
|  |  | Mark the IP DSCP or Precedence Header Fields, Optional | = | ДА |
|  |  | Police the Flow to a Specific Rate with Two-Color Aware Support | = | ДА |
|  |  | RFC 2474: Definition of the Differentiated Services Field (DS field) in the IPv4 and IPv6 Headers | = | ДА |
|  |  | RFC 2475: An Architecture for Differentiated Services | = | ДА |
|  |  | RFC 2597: Assured Forwarding Per-Hop Behavior (PHB) Group | = | ДА |
|  |  | RFC 3246: An Expedited Forwarding PHB | = | ДА |
|  |  | RFC 3260: New Terminology and Clarifications for DiffServ | = | ДА |
|  | Class of Service (CoS) Queue Mapping Configuration | AutoVoIP: Automatic CoS Settings for VoIP | = | ДА |
|  |  | IP DSCP-to-Queue Mapping | = | ДА |
|  |  | Configurable Interface Trust Mode (IEEE 802.1p, DSCP, or Untrusted) | = | ДА |
|  |  | Interface Egress Shaping Rate | = | ДА |
|  |  | Strict Priority versus Weighted Scheduling per Queue | = | ДА |

4. Безжична точка за достъп 4

| Наименование: | Безжична точка за достъп 1 |
| --- | --- |
| Прогнозно количество за една година: | 30 броя |
| Гаранционен срок | >= | 24 месеца |
| ОСНОВНИ ХАРАКТЕРИСТИКИ | Processor Specs | Atheros MIPS 74Kc, 560 MHz | = | ДА |
|  | Cross-pol Isolation | 20 dB Minimum | = | ДА |
|  | Beamwidth | 45° (H-pol) / 45° (V-pol) / 45° (Elevation) | = | ДА |
|  | Polarization | Dual Linear | = | ДА |
|  | Enclosure | UV Resistant Polycarbonate | = | ДА |
|  | Mounting | Pole-Mount (Kit Included) | = | ДА |
|  | Operating Frequency (MHz) | Worldwide | 5150 – 5875 | = | ДА |
|  | Management Radio (MHz) | Worldwide | 2412 – 2472 | = | ДА |
|  | Wi-Fi Standards | 802.11abgn/ac | = | ДА |
|  | Channel Bandwidths | 10/20/30/40/50/60/80 MHz | = | ДА |
|  | Antenna Gain | = | 16 dBi |
|  | Memory DDR2 | >= | 64 MB |
|  | Power Specs | 24V, 0.5A Gigabit PoE Supply (Included) | = | ДА |
|  |  | Power Method | 802.3af Alternative A (Pairs 1, 2+; 3, 6 Return) | = | ДА |
|  |  |  | 24V Passive PoE (Pairs 4, 5+; 7, 8 Return) | = | ДА |
|  |  | Max. Power Consumption | <= | 8,5W |
|  | Networking Interfaces | 10/100/1000 Mbps Ethernet Ports | >= | 2 |
|  | Operating Temperature | -5 to 40° C | = | ДА |
|  | Operating Humidity | 5 to 95% Noncondensing | = | ДА |

Обособена позиция № 4. Фотокопирно устройство

1. Фотокопирно устойство

| Наименование: | Фотокопирно устройство |
| --- | --- |
| Прогнозно количество за една година: | 1 брой |
| Гаранционен срок | >= | 24 месеца |
| ОСНОВНИ ХАРАКТЕРИСТИКИ | Скорост на копиране | Формат А4 | >= | 45 ppm |
|  |  | Формат А3 | >= | 25 ppm |
|  | Контролен панел | Чувствителен на допир | >= | 9 inch |
|  | Разделителна способност / Нива | Сканиране: 600 x 600 dpi | = | ДА |
|  |  | Печат: 600 х 600 dpi; 2,400 x 600 dpi | = | ДА |
|  | Мащабиране | от 25% до 400%, стъпка 1% | = | ДА |
|  | Многократно копиране | 1-999 | = | ДА |
|  | Режими на копиране | Текст, Текст/Фото, Фото, Цветен документ, Custom | = | ДА |
|  | Двустранно копиране | Стандартно | = | ДА |
|  | Основни копирни функции | Електронно сортиране | = | ДА |
|  |  | Авт. увеличение/ намаление | = | ДА |
|  |  | Авт. избор на размер на лист | = | ДА |
|  |  | Energy Saver | = | ДА |
|  |  | X/Y Zoom | = | ДА |
|  |  | Trimming/ Masking | = | ДА |
|  |  | Електронни кодове за достъп | >= | 10000 |
|  |  | Копиране 2 в 1 | = | ДА |
|  |  | Копиране 4 в 1 | = | ДА |
|  |  | Копиране 8 в 1 | = | ДА |
|  |  | Резервиране на задача | = | ДА |
|  |  | Вмъкване на корица | = | ДА |
|  |  | Вмъкване на страница Анотация (дата/час) | = | ДА |
|  | Капацитет на хартия (стд./макс.) | Стандартно: две касети по 550 листа и байпас за 100 листа – общо 1200 листа | = | ДА |
|  |  | Максимално: 3200 листа | = | ДА |
|  | Размер на хартията (мин.- макс.) | A5R-A3 | = | ДА |
|  | Тегло на хартията (касета) | 60-256 g/m2 | = | ДА |
|  | Тегло на хартията (байпас) | 52-256 g/m2 | = | ДА |
|  | Принтер | Памет | >= | 4GB |
|  |  | Хард диск | >= | 320GB |
|  |  | Разделителна способност на принтиране Up to 3600 х 1200 dpi | = | ДА |
|  | Интерфейс | Ethernet 10/100BaseT | = | ДА |
|  |  | USB2.0 (Full Speed) | = | ДА |
|  | Принтерски езици | PCL5e, PCL5c, PCL6 (PCL XL), XPS and PostScript 3 compatible | = | ДА |
|  | Скенер | Черно-бяло: до 240 изображения./мин.(300dpi) | = | ДА |
|  |  | Цветно: до 240 изображения./мин (300dpi) | = | ДА |
|  |  | Капацитет на устройството за автоматично подаване на оригинали | >= | 300 листа |
|  | Консумативи | Поддържане на работа с тонера с капацитет при 5% запълване на страниците | >= | 43 900 копия |
|  | Тегло на основното тяло | <= | 58 кг. |
|  | Конфигурация на устройството | 2 броя касети за по 550 листа | = | ДА |
|  |  | Бай – пас за 100 листа | = | ДА |
|  |  | Мрежов принтер и цветен скенер | = | ДА |
|  |  | Памет | >= | 4 GB |
|  |  | Hard Disk |  | 320 GB |
|  |  | Автоматично реверсивно устройство за двустранно откопиране - ADU | = | ДА |
|  |  | Устройство за автоматично поемане и обръщане на оригиналите - DSDF (капацитет 300 листа) | = | ДА |
|  |  | Шкаф на колелца на който да се постави машината | = | ДА |
|  |  | Вътрешно финиширащо устройство | = | ДА |
|  |  | Перфоратор | = | ДА |